## Slide 1: FASE Framework for Air-Mobility SoS Evaluation
Victor Petitgenet - (vpetitgenet@gatech.edu)
Alex Ostrow - (aostrow7@gatech.edu)
Nadir Ougazzaden - (nadirougazzaden@gatech.edu)
Kaleb Cornick - (kcornick3@gatech.edu)

## Slide 2: Team Members
Academic Advisor
Dr. Mavris
Research Engineer
Dr. Justin
Dr. Christopher Jouannet
Dr. Kristian
Amadori
Graduate Students
Kaleb
Cornick
Alex
Ostrow
Nadir
Ougazzaden
Victor
Petitgenet

## Slide 3: Table of Contents
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 4: Current Situation
Subway | 
Midtown | 23-33 (min)
Buckhead | 32-42 (min)
Sandy Springs | 41-51 (min)
Rideshare or Rental Car | 
Midtown | 22-45 (min)
Buckhead | 30-60 (min)
Sandy Springs | 40-75 (min)
Consider a notional trip between Hartsfield-Jackson Int’l Airport three areas in Atlanta: Midtown, Buckhead, and Sandy Springs
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Travel times within city limits are significantly longer than desired. Whereas it might have taken an hour to fly 600 miles to get into the city, it would take that same hour to travel the last 12 miles to the final destination. As such, there is clearly an issue with the given infrastructure.

## Slide 5: Motivation for Air Mobility
Long time to travel short distances
Shortcomings in transportation system
A new method is needed for mobility in urban areas
Common problem to many urban areas
  Inadequate or limited public transportation
  Congested roadways
Challenging to find solution to this given existing infrastructure
Significant project duration
Significant capital investment
Significant disruption to existing infrastructure
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: These long times to travel short distances indicate shortcomings in the current transportation system, and are largely caused by limited public transportation or congested roadways. While improving the existing infrastructure is desirable, there are significant duration, investment, and disruption considerations that make it challenging. As such, a new method is needed for mobility in urban areas.

## Slide 6: Motivation for Air Mobility
What if a third dimension was added to routes?
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: What if we were to add the third dimension to routes? After all, we have been flying between cities for many years. This is where urban air mobility, or UAM, fits in to the transportation infrastructure.

## Slide 7: Past & Current Implementations
1965
Present Day
Urban Air Mobility isn’t a fundamentally new idea
Flights from Manhattan
to surrounding airports for $43(adjusted)
Flights from lower Manhattan
to J.F.K. airport for $200-225
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: UAM isn’t a fundamentally new idea. As early as the 1960s, companies have been offering services using conventional helicopters as air taxis. These services still exist today, but generally serve a niche market in a small number of cities.

## Slide 8: Past & Current Implementations
Need for a better solution and supporting infrastructure
These implementations are not the solution we are seeking
Increasing public resistance to proliferation of helicopter operations in urban areas
Safety
Concerns
Emission Concerns
Noise
Concerns
Affordability
Concerns
Legislation being proposed to limit urban helicopter activities
  Improving Helicopter Safety Act (2019)
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Although conventional helicopters fulfil the UAM role, they are not the solution we are seeking due to affordability, noise, emission, and safety concerns. There is an increasing public resistance to helicopter operations, so much so that legislation is even being proposed to limit their activities. As such, a better solution and supporting infrastructure is needed.

## Slide 9
Convergence of Enablers
Sensor Technology
Battery Technology
Autonomy
Electric Propulsion
Material Technology
Rapid Development Time
Comm. Networks
Enablers for Urban Air Mobility
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Many emerging technologies allow eVTOL UAM to be considered as a viable alternative, as shown above. Some, like battery technology and autonomy, are propelled by the automotive industry, while others are more aerospace-centric.

## Slide 10
Want to expand upon these studies with
big-picture framework that evaluates and compares CONOPS
Analysis has been done with configuration/CONOPS selected at start
Previous Analyses
Elements have been investigated such as:
Vertiport placement[8]
Vehicle performance & design elements[5][8]
Time savings[7]
Environmental Factors[7]
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Of course this is not the first time UAM has been analyzed. However, much of the analysis has been done with CONOPS/configuration selected at the start, evaluating specific elements. As such, this years GC project seeked to build upon these studies with a big picture framework to evaluate and compare CONOPS.

## Slide 11: Emerging Concepts are Point-Designs
Despite operating in the same emerging markets, physical and functional designs vary greatly between concepts
BLADE
[10]
Bell Nexus
[11]
Volocopter 2X
[12]
Lilium Jet
[13]
On-Demand
Scheduled
Defined Routes
Point-to-Point
vs
vs
Functional
Physical
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Emerging designs differ both functionally and physically
Functional designs range from on demand services to scheduled services, flying defined routes or as true point-to-point air taxis
The vehicles themselves are very dissimilar as well, ranging from fully electric multirotors to hybrid electric tiltrotors

## Slide 12: Challenges in Implementation
Significant challenges associated with modelling and evaluating a SoS due to large number of variables involved
How can we capture a UAM SoS architecture in a manageable way?
How can we evaluate this architecture?
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Given that there are a large number of variables involved, this years GC attempted to capture a UAM SOS in a manageable way and evaluate it.

## Slide 13: How would a SoS be Scoped?
What is the overall purpose of the System-of-Systems?
Who is going to use it, why will they use it, and how will they use it?
What elements does the network consist of?
What does each element interface with (externally and internally)?
What are the functions of each element?
What are the constraints on each element?
Where will the network be located, and what is its physical layout?
What technologies (future or present) will be leveraged to support the system?
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Scoping a general SOS problem would begin by providing the following context:
  Overall purpose
  Stakeholders
  Elements (including interfaces, functions, and constraints)
  Location and Layout
  Technologies leveraged

## Slide 14: Context Required to Scope UAM SoS
- Level of Autonomy
- Maintenance, Repair, & Overhaul
- Pilot Training (If Piloted)
- Noise Output
- Fleet Operations Management
- Airport/Vertiport Infrastructure
- Charging Stations
- Urban Planning/Zoning
- Policy Development
- Ownership (Public/Private)
- Unmanned Traffic Management
- Communications & Navigation
- Flight Procedures
- Data Exchange and Coordination
- Cybersecurity
- Consumer Demand
- Passenger/Cargo Operations
- Affordable Transportation
- On-Demand vs Scheduled
- Vehicle Safety
- Airworthiness Standards
- Certification Processes
- Public Acceptance
- Implementation Roadmap
Vehicle
Airspace
Economics
Infrastructure
Regulations
[9] Briceno, Simon. Urban Air Mobility: What is it and how soon? Georgia Airports Association Annual Conference and Exposition, September 2019
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: More context is required to scope a UAM SOS problem, falling into 5 key categories:
  Vehicle
  Infrastructure
  Airspace
  Regulations
  Economics

## Slide 15: Research Question
The methodology must satisfy the following:
Flexible to allow assessment of different SoS
Parametric environment to allow user adjustment
Given that the design space for a UAM SoS is unmanageably large, how can we support decision-making and evaluation?
High level outputs allowing for comparisons
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Research question attempts to intelligently restrict the design space so decision making and evaluation can be done for a UAM SOS

## Slide 16: Methodology Introduction
Evaluating a UAM SoS is inherently reliant on data and mathematical relationships, but need a way to ensure credible results
Methodology developed in UAM context, but for use across general SoS problems
Importance of defining a methodology beforehand
Interested in a modelling & simulation approach
Need defined methodology for results to be meaningful and reproducible
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Methodology must be defined early on in order for results to be meaningful and reproducable
Methodology developed in UAM context, but for use across general SOS problems (not constrained to UAM)

## Slide 17: Methodology Roadmap
Selecting a Perspective
Understand and Scope System of System Goals
Develop / Identify Evaluation Criteria
Decompose Evaluation Criteria
Create Simulation Environment
Generate and Analyze Results
Alex Ostrow
Iterate Until Desired Fidelity Achieved
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
1
2
3
4
5
6
Notes: Iterative process, illustrated in further detail

## Slide 18: Selecting a Stakeholder Perspective
Need to define stakeholder perspective at beginning to determine evaluation criteria
Different stakeholders have different needs and standards by which they evaluate a SoS
Operators
Operating Costs
Manufacturers
Demand
Customers
Time Savings
Example Stakeholders and Associated Criteria for a UAM SoS
City Planners
Regulators
Safety
Environmental Impact
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Different stakeholders will evaluate a SOS differently, so is important to select one early
This drives the SOS goals chosen and evaluation criteria

## Slide 19: SoS Goals and Evaluation Criteria
SoS alternatives can take the form of dissimilar architectures
Surveillance
Example
vs
Need to identify SoS goals that are independent of a specific implementation
Criteria #1
Criteria #2
Criteria #3
Criteria #4
(Specific, measurable quantities)
Map each goal to one or more evaluation criteria
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: SOS alternatives can be very different, but achieve the same goal
Therefore the goal must be identified independent of a specific implementation, and mapped to evaluation criteria

## Slide 20: Breakdown of Evaluation Criteria
High level SoS goals
Breakdown
SoS Variables
How can you link the SoS variables to the high-level goals?
What level of a breakdown is required?
How many variables should be retained in the breakdown?
Need for a structured and systematic approach to the breakdown
Breakdown is a highly nontrivial exercise
Alex Ostrow
Evaluation Criteria
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Evaluation criteria are broken down to make up the SOS variable set, or the design variables that describe the SOS
This breakdown exercise must be done in a systematic and structured way to retain only the appropriate variable set

## Slide 21: Simulation Environment
Alex Ostrow
Evaluation Criteria #1
Evaluation Criteria #2
Evaluation Criteria #m
…
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
SoS Design Variable #1
SoS Design Variable #2
SoS Design Variable #n
…
Link resulting breakdown in simulation environment
Notes: After the evaluation criteria are broken down into variables and functions, they can be linked in a simulation environment

## Slide 22: Analysis & Iterations
Assumption that models capture true behavior of SoS
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Design of Experiments
R1
xi
R2
xj
Highly Sensitive, Candidate for More Detailed Model
Develop More Detailed Model
Insensitive Response, No Need For Additional Modeling Capability
Integrate Updated Model into Simulation Environment
Notes: In order to evaluate whether a model requires further fidelity, an initial design of experiments is performed over the entire design space
Examining trends, and sensitivities
If a response is highly sensitive to a simplistic model, it is a likely candidate for a further detailed model

## Slide 23: Intended Use
Alex Ostrow
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Simulation environment is a decision-making tool after development
Use simulation environment to make initial decisions
Fix chosen configuration as baseline and explore design space
Create surrogates and make final design adjustments
Notes: Overall intended use of the methodology is to produce a decision-making tool to select between CONOPS

## Slide 24: Perspective Selected for Implementation
Victor Petitgenet
                Different objectives
                Different relevant metrics
Who is using the methodology?
City council decision-maker
Responsible for evaluating which UAM SoS to implement, if any, for an airport shuttle use case
Benefits vs. Costs Assessment
Who is benefitting ?
What are the benefits?
What is the societal impact?
Who will be adversely impacted?
Subsequent steps in the methodology are informed by contextual information
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Selected point of view of a city council decision maker for implementation
Imagining city this decision maker is going to be making a series of cost vs benefit assessments regarding implementing this SoS

## Slide 25: Identification of SoS Goals
Enables the development of complex architectures and facilitates decision making through information sharing
DoDAF & FAA EA
Victor Petitgenet
Goals
Questions
Metrics
GQM Approach
Data
Data
Enables the understanding of the impact of architecture-level decisions, focus on executable products
ARCHITECT Process
Understand SoS architecture to facilitate evaluation criteria identification
Retained GQM from ARCHITECT to guide subsequent breakdown exercise
OV-1
OV-2
OV-3
Creation of a series of static views
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Explored DODAF and FAA EA to better understand SoS
Not very useful since they’re focused on static products
Interested in the ARCHITECT process where there is a focus on an executable product

## Slide 26: Identifying Evaluation Criteria
UAM provides an alternate transportation solution to decrease travel time at an acceptable cost while minimizing adverse societal impact
Time Savings
Affordability
Societal Impact
Victor Petitgenet
Goals
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Returning to the original motivation statement for UAM
From this statement, there are three goals that can be translated to evaluation criteria

## Slide 27: Breakdown: “Bottom-Up” Approach
Approach Steps
Discern categories
List elements
Interlink elements
Link elements to eval. criteria
Inadequate Method
Victor Petitgenet
Vehicle
Infrastructure
Economics
Operations
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Explored a top down approach to decompose the evaluation criteria into the SoS variables
Step to this approach shown
Ultimately deemed this approach to be inadequate

## Slide 28: Breakdown: “Top-Down” Approach
Different types of elements
Different levels of elements
Vague element definitions
Unclear links between elements
Downsides of ”Bottom-Up”
“Top-Down” Approach
Identify specific evaluation criteria
Assign mathematical relationships to evaluation criteria
Identify relevant variables
Decompose variables (as required)
Link variables
“Top-Down” Approach
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Reasons for deeming the bottom-up approach to be inadequate shown
Thus, switch to using a top-down approach
Steps to top-down approach shown

## Slide 29: Evaluation Criteria Definitions
Victor Petitgenet
Population Cumulative Time Savings
Required Average Yield per Revenue Pax Mile
Overall Societal Impact
Total amount of time saved by users of UAM network
Assesses overall effectiveness of a UAM network
Comparison with existing methods of transportation
Amount an operator must charge paying passengers to break even
Assesses affordability, especially from customer perspective
Total population exposed to at least a given noise level
Assesses societal acceptability of a UAM network
Units are hours
Units are cents/pax/mile
Units are # people
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Selected three shown evaluation criteria for the remainder of this implementation

## Slide 30: Cost & Time Savings
Region of Operation
Origin
Destination
Average Route Distance
Vehicle Characteristics
Mission Profile
Average UAM Speed
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Cost
Time Savings
Notes: Example of the mathematical relationships associated to each of the evaluation criteria
As seen, these can begin to be notionally decomposed

## Slide 31: Evaluation Criteria: Societal Impact
No single, direct measure of societal impact
Noise
Emissions
Noise is a key concern for the implementation of a UAM network
Rotational Noise
Vehicle Weight | Number of Rotors | Number of Blades
Rotor Torque | Tip Mach Number | Rotor Solidity
Rotor Angular Velocity | Thrust Loading | Rotor Thick. to Chord
Route Characteristics
Distance to observer
Mission Profile
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Visual Pollution
Notes: Societal impact is a more nuanced evaluation criteria to measure, many different possible meanings
Focusing on noise, specifically rotational noise for this implementation
Showing notional breakdown of noise

## Slide 32: How much information is needed?
Model could range from “back-of-the-envelope”
to full physics-based system model
Necessary to decompose each evaluation
criterion to an appropriately low level
Need to be able to navigate through various levels of
information fidelity and still be able to get meaningful results
“Appropriately low level” means different things to different people; SME might only need a few specific values to determine if a system is viable, while others might need to define entire system before assessment can be made
What is the necessary level of information fidelity?
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Leads to the question of how much information is needed
What is the necessary level of information fidelity ?
Different answers depending on the selected perspective

## Slide 33: SoS Decomposition Levels
Specific Implementation
Engineering / Physics
Decreasing Complexity
Increasing Specificity
Network
Evaluation Criteria
Mission Ranges
Passenger Demand
Total Operating Cost
Rotor Material
Communication Protocol
Airframe Component Weights
Example Measurable Quantities
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Showing example of possible decomposition levels
Network is the highest level
Specific implementation contains high level variables
Engineering/Physics contains the lowest level, most granular variables

## Slide 34: Environment Creation
Victor Petitgenet
Need modules allowing for calculation of Evaluation Criteria that are interlinked
Time Savings
Cost
Societal Impact
Inputs
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Proprietary Time Savings Module
Proprietary Cost Module
Proprietary Societal Impact Module
Static Implementation
Sensitivity
Analysis
Environment
Research and Calibration Data
X %
X %
X %
X %
X %
X %
SoS Sensitivities
Notes: Need to develop modules that allow for the calculation of the evaluation criteria
Connect these modules to form an environment
Methodology is flexible to the user plugging in their own modules
Initially a static implementation but want to transition to being able to perform sensitivity studies

## Slide 35: DoE Setup
Victor Petitgenet
Use the environment to conduct a DoE around a fixed vertiport layout
Parameter | Low | High
SPL Threshold | 52 | 85
Vehicle Cruise Speed | 100 | 200
Vehicle Mass | 900 | 1500
Landing Fees | 37.5 | 62.5
… | … | …
Using bounds of ±25% around baseline value in most cases
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Notes: Set up a DOE around a fixed vertiport layout
±25% for most variables

## Slide 36: Environment Verification
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Presence of certain trends indicates models are working as expected
Sound Pressure Level Threshold
Population Impacted
Population Impacted vs.
Sound Pressure Level Threshold
PCTS
Vertiport Radius
PCTS vs. Vertiport Radius
Focus is on verifying trends, not specific values
Notes: From DoE, were able to obtain results that showed that the models were working as expected

## Slide 37: Response Sensitivities
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Design of Experiments
R1
xi
R2
xj
High Sensitivity:
Candidate for refined modelling
$/RPM
Battery Size
PCTS
Demand
Is refining this model feasible?
Is refining this model worthwhile?

## Slide 38: Modeling Time-Dependent Demand
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Demand over Time-of-Day
Travel Time over Time-of-Day
Xx:##
Xx:##
Yy:##
Zz:##
Zz:##
X
Y
Z
ATL Departures for ~1 week binned into 1-hour slots
Curve shifted -2 hours to yield VP departure times
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 0 | 0 | 0 | 0.008246 | 0.016149 | 0.040714 | 0.084349 | 0.093455 | 0.09397 | 0.05944 | 0.074042 | 0.065624 | 0.058925 | 0.083835 | 0.073527 | 0.063734 | 0.042261 | 0.044322 | 0.023364 | 0.029205 | 0.030579 | 0.010308 | 0.0029205 | 0.0010308
Default travel time modeled as additional time for rush hour, less time normally
Demand
Travel Time
Time of Day
Travel Time
Time of Day
Notes: Switching from a constant demand throughout the day to a time dependent demand, using departure data from Atlanta airport
Also model increase in travel time due to rush hour

## Slide 39: Generating Network Alternatives
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
“Inside the Perimeter”
“Outside The Perimeter”
VP Locations
Midtown
Buckhead
Decatur
Vinings
VP Locations
Marietta
Smyrna
Sandy Springs
Roswell
Alpharetta
Duluth
Dekalb
“Close/Far Mix”
“Targeted Demand”
VP Locations
Midtown
Buckhead
Sandy Springs
Alpharetta
VP Locations
Midtown
Decatur
Marietta
Roswell
Alpharetta
Duluth
Dekalb
After environment was completed, network alternatives were generated from combining vertiport layouts and vehicle types
Notes: Generated a series of 4 vertiport layout alternatives

## Slide 40: Generating Network Alternatives
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Vehicle types approximately resemble existing designs
“Light” Vehicle
“Medium” Vehicle
“Heavy” Vehicle
Design Variable | Value (autonomous)
Cruise Speed | 60 kts
Pax Capacity | 1 (2)
Number of Rotors | 24
Total Mass | 800 kg
Cost/Vehicle | $500,000 ($1,000,000)
Design Variable | Value (autonomous)
Cruise Speed | 100 kts
Pax Capacity | 3 (4)
Number of Rotors | 12
Total Mass | 1000 kg
Cost/Vehicle | $1,000,000 ($1,500,000)
Design Variable | Value (autonomous)
Cruise Speed | 150 kts
Pax Capacity | 5 (6)
Number of Rotors | 6
Total Mass | 1200 kg
Cost/Vehicle | $2,000,000 ($2,500,000)
Notes: Generated a series of 6 total vehicle alternatives, loosely based on existing designs

## Slide 41: Analyzing Network Alternatives
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
 | Light Piloted Vehicle | Light Auto Vehicle | Medium Piloted Vehicle | Medium Auto Vehicle | Heavy Piloted Vehicle | Heavy Auto Vehicle
ITP Config | X | X | X | X | X | X
OTP Config | X | X | X | X | X | X
Target. Demand Config | X | X | X | X | X | X
Close/Far Mix Config | X | X | X | X | X | X
PCTS
$RPM
Population Impacted
24 Unique Configurations
Evaluation criteria for each UAM network calculated using environment
Notes: Total of 24 alternatives that were run through the environment in order to obtain the calculations for the evaluation criteria

## Slide 42: Analyzing Network Alternatives
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Population Cumulative Time Savings
$/RPM
“Inside The Perimeter (ITP)” and “Targeted Demand”
More demand, less time savings per flight
Increasing vehicle size
“Outside The Perimeter (OTP)” and “Close/Far Mix”
Less demand, significant time savings per flight
Increasing vehicle size
Population Impacted
$/RPM
“OTP” and “Close/Far Mix”, Med/Heavy Vehicle
Farther routes, noisier vehicle
Notes: From the resulting 24 configurations some general trends were discovered, most notably depending on whether the operation is inside the perimeter or outside the perimeter significantly impacts the PCTS. $/RPM tends to decrease as vehicle size increases due to the dispersion of operating cost across more passengers. A larger vehicle is also correlated with a higher population effected.

## Slide 43: Analyzing Network Alternatives
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Population Impacted
Population Cumulative Time Savings
“OTP” and “Close/Far Mix”, Light Vehicle
Farther routes, less noisy vehicle
“OTP” and “Close/Far Mix”, Med/Heavy Vehicle
Farther routes, noisier vehicle
“ITP” and “Targeted Demand”
Shorter routes, less area covered
Increasing vehicle size
Increasing vehicle size
“Medium” Vehicle captures the same benefits of “Heavy” Vehicle at lower $/RPM
“Light” Vehicle in a high-demand, long range routes cannot sustain demand
Impact of autonomy is less obvious as vehicle capacity increases
Key Takeaways
Notes: Echoing the aforementioned trends, PCTS is significantly effected by the OTP routes as there is a much larger time savings per trip but at a lower demand level.

## Slide 44: Refined Selection
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Evaluation criteria used to select best alternative
Autonomous “Medium” Vehicle
“Close/Far Mix” Config.
PCTS: 62830
(hours)
$/RPM: 9.4795 ($/pax/mile)
Pop. Imp: 37944 (people)
Perform final DoE around selected alternative
±10% around all design variables
Create surrogate models for evaluation criteria
Explore sensitivity of Evaluation Criteria
May be necessary to create multiple sets of surrogate models depending on alternatives being compared
UAM Airport Shuttle
UAM Air Taxi
vs.
UAM Airport Shuttle
UAM Airport Shuttle
vs.
Single Set
Multiple Sets
Notes: Selected the Autonomous ”med” vehicle as the most favorable alternative with the close/far vertiport config
Performed final DoE around this layout
Explaining necessary steps if we wanted to consider dissimilar CONOPS, comparing similar CONOPS for this implementation although methodology is flexible

## Slide 45: Tying in the 5 Categories
Capability to assess overall importance in addition to specific sensitivities
Victor Petitgenet
Allow decision maker to focus their efforts on relevant areas
Determine the overall sensitivity of an evaluation criteria to a given area
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
$/RPM
Chart: Percent Contribution
| Vehicle | Economics | Airspace | Regulations | Infastructure
$/RPM | 1.2049 | 23.5146 | 0.097168 | 0.02915 | 75.1543
Pop. Cumulative Time Savings
Chart: Percent Contribution
| Vehicle | Economics | Airspace | Regulations | Infastructure
PCTS | 0.097741 | 49.8292 | 0.0088856 | 0.0088856 | 50.0553
Population Impacted
Chart: Percent Contribution
| Vehicle | Economics | Airspace | Regulations | Infastructure
Pop_Effected | 3.0478 | 0.14308 | 0.0392 | 96.7249 | 0.045079
Notes: Also want to be able to aggregate the sensitivities of the evaluation criteria to the 5 key areas of UAM
Showing results from aggregating sensitivities

## Slide 46: Dashboard
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Connected environment to a dashboard for decision-making support
Vertiport
Placement
SoS
Design
Design Space
Exploration
Design
Selection
4-tabbed Interface:
Vertiport Placement Tab:
User places vertiport(s) using Lat/Lon Pairs & default travel time:
Victor Petitgenet
Notes: Paired the developed environment with a GUI to facilitate decision-making
Follows 4-tabbed layout
Vertiport placement tab allows user to place any number of vertiports using lat/lon pairs

## Slide 47: Dashboard
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
User generates SoS design alternatives using sliders
Results for selected design shown on 3-axis plot
Possibility to set variables to default values
SoS Design Tab:
Victor Petitgenet
Notes: SoS design tab gives the user the ability to design any number of SoS alternatives using the provided sliders

## Slide 48: Dashboard
User investigates performance of SoS design alternatives
Design Space Exploration Tab:
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
2D and 3D Eval. Criteria Plots:
Eval. Criteria values & Key Design Variables:
Victor Petitgenet
Notes: Design Space exploration tab allows the user to visualize the performance of the different SoS alternatives from the point of view of the evaluation criteria

## Slide 49: Dashboard
Multi-Attribute Decision Making Technique used to recommend a SoS Design
Design Selection Tab:
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
User inputs weighting scheme:
Victor Petitgenet
Interface recommends a design:
Notes: Design selection tab implements a MADM technique along with a user defined weighting scheme to recommend a design

## Slide 50: Closing the Loop
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Developed a methodology to make an unmanageable decision-making process more manageable by intelligently restricting the design space of interest
Paired with an environment and user interface that allows for comparison of different alternatives or scenarios based on evaluation criteria
Make a decision regarding the SoS architecture
Provide insight regarding importance of 5 key UAM areas
Notes: Developed a methodology to answer the original research question
Implemented this methodology for the use case of a UAM airport shuttle, able to recommend a SoS design
Also able to give insight into the sensitivities of the evaluation criteria with respect to the 5 key areas

## Slide 51: References
[1] Image Credit: https://www.itsmarta.com/train-stations-and-schedules.aspx
[2] Image Credit: https://i2.wp.com/vintageairliners.com/wp-content/uploads/2015/06/tumblr_npqg5tRdbQ1skp1rlo1_1280.jpg?ssl=1
[3] Image Credit: https://i2.wp.com/vintageairliners.com/wp-content/uploads/2015/06/tumblr_npqg5tRdbQ1skp1rlo4_540.jpg?ssl=1
[4] Image Credit: https://www.uber.com/blog/new-york-city/uber-copter/
[5] https://maloney.house.gov/media-center/press-releases/reps-maloney-nadler-velazquez-introduce-legislation-to-address-nyc-s
[6] VTOL Urban Air Mobility Concept Vehicles for Technology Development
[7] Environment Impact on Feasibility of Sub-Urban Air Mobility using STOL Vehicles
[8] Door-to-Door Travel Time Comparative Assessment for Conventional Transportation Methods and Short Takeoff and Landing On Demand Mobility Concepts
[9] Progress in Vertiport Placement and Estimating Aircraft Range Requirements for eVTOL Daily Commuting
[10] Image Credit: https://blade.flyblade.com
[11] Image Credit https://www.bellflight.com/products/bell-nexus
[12] Image Credit https://www.volocopter.com/en/
[13] Image Credit https://lilium.com/
[14] Briceno, Simon. "Urban Air Mobility: What is it and how soon?" Georgia Airports Association Annual Conference and Exposition, September 2019, Jekyll Island Convention Center, Jekyll Island, GA.
[15] https://www.asdl.gatech.edu/ARCHITECT.html
[16] https://www.airbus.com/careers/working-for-airbus/innovations-of-tomorrow.html
[17] VertiportPlacementForeVTOLCommuting.pdf
[18] A Vehicle Demand and Optimization Model for On-Demand Aviation (Brown and Harris)

## Slide 52: Backup

## Slide 53: Common Inputs to Evaluation Criteria
Region
(Urban area of interest)
Origin / Destination
( Latitude – Longitude pairs)
Default Method of Transportation
(comparison with train, automobile, …)
Mission Profile / Operations
(Sortie Rate, Turnaround Time…)
Route Type
(Airport Shuttle, Air Taxi, etc)
Affordability
(Income level of target population)
Vehicle Characteristics
(Cruise Speed, Range, Capacity…)
Accessibility
(Acceptable distance around vertiports)
Decomposition of evaluation criteria yielded common inputs
Need to determine values/methods to generate values for these common inputs
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 54: Input Data Sources – Demand
Household Income level (x1000) | Average Flights per year (2017)
<25 | 1.0
25-49 | 0.9
50-74 | 1.7
75-99 | 5.1
100-149 | 3.2
>150 | 5.4
Demand modelling incorporates census and economic data
Census Data
Economic Surveys
Demand mapped to geographic area
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 55: Input Data Sources – Performance
Vehicle | Max Range | Speed | Capacity | Energy Source
Bell Nexus | 130 nm | 155 kts | 4+1 | Hybrid Electric
Volocopter X2 | 14.5 nm | 55 kts | 2+0 | Electric
A3 Vahana | 54 nm | 125 kts | 2+0 | Electric
Aurora Flight Sciences PAV | 43 nm | 97 kts | 2+0 | Electric
Pipistrel 801 | 52 nm | 152 kts | 4+1 | Electric
Karem Butterfly | 73 nm | 130-175 kts | 4+1 | Electric
Joby S4 | 130 nm | 120 kts | 4 | Electric
Airbus CityAirbus | 16 nm | 65 kts | 4 | Electric
Performance modelling uses existing/upcoming vehicles to estimate values
Input ranges for performance parameters bounded by realistic values
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 56: Time Savings Module
Quantify time savings by comparing travel times with/without UAM networks
Calculates time savings as a function of geographical/population data and vehicle specs
Region GIS/Census Data
Origin / Destination Points
Default Travel Time (without UAM)
Vehicle Characteristics
Population Cumulative Time Savings
Demand per Income Level
Time Savings Module
Area served by VP
Direct point-to-point flight
X1 min
X2 min
X3 min
X4 min
Takeoff
Landing
Getting to VP
Cruise Segment
Number of Required Vehicles
Total Number of Flights
Flight Distances
To other modules:
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 57: Cost Module
Using $/RPM as a proxy for the cost to the consumer
Vehicle Characteristics
Laborers
# of Vehicles from Time Savings Module
General Taxes
Materials/Deterioration Maintenance
DOC
Module
IOC
Module
Vertiport
Laborers
Vehicle
General Taxes
Landing Fees
Insurance
Flight Distances from Time Savings Module
Vehicle Characteristics
Demand per Income Level
Load Factor
# Seats
Distance
Calculates $/RPM as a function of DOC, IOC, Number of Seats, Distance, and Load Factor
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 58: Societal Impact Module
Quantify societal impact by counting number of people exposed to at least a given noise level
Vehicle Noise Output
Ground Track
Vortex noise is the primary noise source for an eVTOL vehicle
Leverage previously developed noise model[18]
Constant | 
Rotor Tip Speed | 
Air Density | 
Constant | 
Rotor Tip Speed | 
Air Density | 
# of Rotors | 
Thrust (= Weight) | 
Rotor Solidity | 
Thrust Loading | 
# of Rotors | 
Thrust (= Weight) | 
Rotor Solidity | 
Thrust Loading | 
Vehicle Characteristics
Distance
Able to calculate noise SPL as function of distance for given vehicle
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 59: Societal Impact Module
Defining a SPL threshold and altitude gives a radius of impact for the vehicle
Pair with flight path to find noise “footprint”
Area of intersection between footprint and ith planning region
Population density of ith planning region
Victor Petitgenet
R
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 60: Environment Details
Region
(Urban area of interest)
Origin / Destination
( Latitude – Longitude pairs)
Default Method of Transportation
(comparison with train, automobile, …)
Mission Profile / Operations
(Sortie Rate, Turnaround Time…)
Route Type
(Airport Shuttle, Air Taxi, etc)
Affordability
(Income level of target population)
Vehicle Characteristics
(Cruise Speed, Capacity…)
Accessibility
(Acceptable distance around vertiports)
Static Implementation
Sensitivity
Analysis
Analysis Environment
Research and Calibration Data
Cost
Time Savings
Env. Impact
Evaluation Criteria
X %
X %
X %
X %
X %
X %
SoS Sensitivities
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions

## Slide 61: Results from Updated Demand Model
Victor Petitgenet
Methodology
Implementation
Motivation
Current Methods
Dashboard
Conclusions
Overall demand for flights unchanged…
…But lower-level design variables have less impact on time savings overall
PCTS
Demand
PCTS
Normalized demand at 7 AM
Lower-level variables in demand model prove to be less sensitive